## Slide 1: Radio Astronomy at Home
Aaron Clevenson
NARS
August 15, 2025

## Slide 2: Agenda
What is Radio Astronomy
What the Pros Use
What Can We Do at Home
    Itty-Bitty Telescope
    Super SID
    Meteor Observing
    Radio Jove
    Milky Way Galaxy

## Slide 3: Visible Light Astronomy
Most Amateur Astronomers Observe Visible Light

## Slide 4: Electromagnetic Spectrum
But Light (Electromagnetic Radiation) is much more than just Visible Light
Visible Light
Radio Waves
IR
UV
X-Ray
Gamma Rays

## Slide 5: Observing Beyond the Visible
How Astronomers Do It
Radio Waves
IR
UV
X-Ray
Gamma Rays
Radio Waves
IR
UV
X-Ray
Gamma Rays
James Webb
Chandra
IUE
Hubble
Compton

## Slide 6: But… Some of it is filtered out by the atmosphere

## Slide 7: Observing Beyond the Visible
How Astronomers Do It – Radio Waves
Radio Waves
IR
UV
X-Ray
Gamma Rays
Radio Waves
IR
UV
X-Ray
Gamma Rays
Green Bank
VLA
FAST
VLBA

## Slide 8: Radio Frequencies
30 GHz
3000 GHz
3 GHz
30 GHz
Itty-Bitty Telescope – 12 GHz
0.3 GHz
3 GHz
Milky Way – 1.43 GHz
0.03 GHz
0.3 GHz
Radio Meteors – 0.2 GHz
0 GHz
0.03 GHz
Super SID –
0.000025 GHz (25,000 Hz)
Radio Jove –
0.02 GHz

## Slide 9: Amateur Radio Astronomy
For us to do Radio Astronomy -
We need it to be:
Inexpensive
Not too Big
Easy to Build
Easy to Use
Fun to Do

## Slide 10: What Objects Can We Observe
The Sun
Jupiter
Meteors
Solar X-Ray Flares
The Milky Way

## Slide 11: The Tools We Can Use
The Sun – Radio Jove, Itty-Bitty Telescope
Jupiter – Radio Jove
Meteors – FM Radio
Solar X-Ray Flares – Super SID
Milky Way – Horn antenna

## Slide 12: The Itty-Bitty Telescope
Detect the Sun
Detect Humans
Low Resolution
Uses a TV Dish
http://www.setileague.org/articles/lbt.pdf

12 GHz

## Slide 13: The Itty-Bitty Telescope
Parts needed
  TV Dish
  Signal Meter
  Battery Pack
http://www.setileague.org/articles/lbt.pdf

## Slide 14: Radio Jove
Detect Jupiter
Detect the Sun
Dipole Antenna
http://radiojove.gsfc.nasa.gov/help/

20.1 MHz

## Slide 15: Radio Jove
Signals
Jupiter Signals: L burst (top), S burst (bottom)
Sun Signal: Solar burst

## Slide 16: Radio Jove
Parts needed
  4 Masts and guy wires
  2 Dipole Antennas
  Receiver
  Computer
  Speakers

## Slide 17: Radio Jove
The Antennas

## Slide 18: FM Radio - Meteors
FM Radio or Radio Dongle for the Computer
Software to record and display signals
Antenna
http://www.skyscan.ca/meteor_radio_detection.htm


## Slide 19: FM Radio - Meteors
Buy the computer radio dongle
Build the Antenna
Listen
200 MHz

## Slide 20: FM Radio - Meteors
My Success

## Slide 21: FM Radio - Meteors
Parts Needed
  Antenna
  Radio Dongle
  Computer

## Slide 22: FM Radio - Meteors
Yagi Antenna Design

## Slide 23: Super SID
Hardware to bring the signal to your computer
Software on computer
Antenna
0.025 MHz


## Slide 24: Super SID
What the computer sees
  Updated every 5 seconds
  A Day with no Flares
LaMoure, ND, 25.2 kHz
Cutler, ME, 24.0 kHz

## Slide 25: Super SID
Results – Not so good
Extremely Low
Frequency

## Slide 26: Super SID
X-Ray Flares on the Sun
Radiation Ionizes Atoms in the Ionosphere
Distant Very Low Frequency Radio Signals are Reflected by Free Electrons in the Ionosphere

## Slide 27: Super SID
What you see…
  A quiet day
  Flares detected
  Lightening
  Off-Air



X

## Slide 28: The Milky Way
Horn Antenna
Radio Receiver
1 gallon “paint thinner” can
Horn Antenna, cardboard and
Aluminum foil
Electronics

## Slide 29: The Milky Way
Results of sky scan

## Slide 30: The Milky Way
Antenna Dimensions
1,430 MHz

## Slide 31: The Milky Way
Electronics Details

## Slide 32: The Astronomical League www.astroleague.org
Radio Astronomy Observing Program
Bronze, Silver and Gold Levels
1, 2, and 4 Techniques Respectively

## Slide 33: Questions aaron@clevenson.org
?