## Slide 1: Portable Solar Power
Presented by
Ron Matusek - WA6TQH
Paul Kent – KI5FJS
Amateur Radio Portable Power Solutions

## Slide 2: Project Objective
To promote community wide understanding of the amateur radio communications service when operating off grid while being available to the public during times of emergency or natural disaster. Alternate power sources are available to power the radio, generators, battery power, solar power and combinations there of. To organize and train members capable of maintaining communications during emergencies as a public service.
Field Day is a showcase for how amateur radio works reliably under any conditions from almost any location to create an independent communications network. “Ham radio functions completely independent of the Internet or cell phone infrastructure, can interface with laptops or smartphones, and can be set up almost anywhere in minutes. Most importantly amateur radio stations can operate independently of the local electrical grid. i.e. Solar/battery power.

## Slide 3: ICOM IC-7300 HF Transceiver
IC-7300 – The Innovative HF Transceiver with High Performance Real-Time Spectrum Scope

## Slide 4: IC-7300 Power Requirements
Portable Power Requirements |  |  |  |  |  |  |  | 
1 | Radio IC-7300 |  |  |  |  |  | Nom | 
 | a. Power supply requirement: 13.8 V DC (±15%) |  |  |  |  |  | 13.8 | V
 | b. Power consumption: Receive Standby 0.9 A |  |  |  |  |  | 0.9 | A
 | c. Maximum audio 1.25 A |  |  |  |  |  | 1.25 | A
 | d. Transmit Maximum power 21.0 A |  |  |  |  |  | 21 | A
 | e. Transmit Maximum RF 100 Watts |  |  |  |  |  | 100 | Wout
 | f. DC power on transmit |  |  |  |  |  | 289.8 | Win
 | g. RF Pwr Amp efficiency |  |  |  |  |  | 34.51% | 
 | h. Duty Cycle, Tx to Rx ratio/min. |  |  |  |  |  |  | 
 | Assume CQ, CQ, CQ, Callsign, |  |  |  |  |  |  | 

## Slide 5: Dell Inspiron 7706 2n1 Laptop
Dell Inspiron 7706 2n1 Laptop |  |  | 
a. 8 hours /Li-Ion 4 cells 68 Whr (340 grams, 233 x 95.9 X 7.05mm) |  |  | 
b. Processor wattage 28W |  |  | 
c. Input current (maximum) 1.50A (Power adapter) |  |  | 
d. Output current (continuous) 4.62A (Power adapter) |  |  | 
e. Battery 4-cell 68 Wh “smart” lithium-ion |  |  | 
f. Battery voltage 15.20 VDC |  |  | 

## Slide 6: Base Battery Requirements
2 | Bioenno Power BLF-1240A LiFePO4 Battery |  |  |  | 
 | a. Charging Voltage 14.6V |  |  | 14.6 | Vstart
 | b. Charging Current 6A |  |  |  | 
 | c. Open Circuit Voltage |  |  | 10 | Vend
 | d. Maximum Continuous Discharge Current 40A |  |  |  | 
 | e. Maximum Peak Pulse Current 80A (5 sec.) |  |  |  | 
 | f. The maximum continuous discharge current is 40A |  |  |  | 

## Slide 7: Solar Charge Controller
3 | Bioenno Power SC-4830JUD CC/CV Series – Solar Charge Controller |  |  |  |  | 
 | a. Rated Voltage: 12V/24V/36V/48V |  |  |  | 12 | V
 | b. 30A Maximum Load Current |  |  |  | 30 | A
 | c. Input Voltage Range: <50V* |  |  |  | 12 | V
 | d. Load Disconnect: 9.9V/11.2V/13.2V/14V (Depending on voltage of system) |  |  |  |  | 

## Slide 8: Solar Panel BSP-120
4 | Bioenno Power 120 Watt Foldable Solar Panel for Charging Power Packs (BSP-120) |  |  | 
 | a. Maximum Voltage: 18V, Open Circuit Voltage: 22V |  | 18 | V
 | b. Maximum Current: 3.35A (per panel, so 6.7A in parallel) |  | 3.35 | A

## Slide 9: Boost Converter for PC
5a | Step Up Boost Converter Module Adjustable Power Voltage (Use with Laptop Computer) |  |  |  |  | 
 | a. 150W DC-DC 10-32V to 12-35V |  |  |  |  | 
 | b. Computer requires operating voltage of 19.5VDC |  |  |  |  | 

## Slide 10: Recommended Battery Charger
9 | Home Battery Charger: |  |  |  |  |  |  |  |  | 
 | Bioenno Power 14.6V, 10A AC-to-DC Charger (Anderson) for 12V LiFePO4 Lithium Iron Phosphate Batteries (BPC-1510A) |  |  |  |  |  |  |  |  | 

## Slide 11: Typical Breadboard Configuration

## Slide 12: Recommended Battery Case
MEGAbox for 30-70Ah Lithium Deluxe Box

## Slide 13: Component Layout

## Slide 14: Power Analyzer
Powerwerx Wattmeter-PP DC Inline Power Analyzer, 45A Continuous

## Slide 15: Project Parts List Page 1 of 5
Description | Quantity | Source | Number | Cost |  | Basic Parts Needed | Alternate | Source
MEGAbox for 30-70Ah Lithium Deluxe Box | 1 | Amazon |  | $195.95 |  | MEGAbox basic-BLK | $109.99 | Powerwerx
Bioenno Power 12V, 40Ah LFP LiFePO4 Lithium Iron Phosphate Battery | 1 | Amazon | PVC, BLF-1240A | $413.99 |  | Bioenno Power 12V, 20Ah LFP LiFePO4 Lithium Iron Phosphate Battery | $192.99 | Powerwerx
Bioenno Power 14.6V, 10A AC-to-DC Charger | 1 | Amazon | BPC-1510A | $63.34 |  | Bioenno Power 14.6V, 10A AC-to-DC Charger | $48.99 | Powerwerx
Powerwerx Wattmeter-PP DC Inline Power Analyzer, 45A Continuous | 1 | Amazon | Wattmeter-PP | $64.49 |  | Optional |  | 
Bioenno Power 12V/24V/36V/48, 30A Universal Solar Charge Controller | 1 | Amazon | SC-4830JUD | $87.39 |  | Bioenno Power 12V/24V/36V/48, 20A Universal Solar Charge Controller | $64.44 | 

## Slide 16: Parts List Page 2 of 5
 | Bioenno Power 120 Watt Foldable Solar Panel | 1 | Amazon | BSP-120 | $236.94 |  | Bioenno Power 120 Watt Foldable Solar Panel | $236.94 | 
 | Powerwerx PanelPole1, Panel Mount Housing | 1 | Amazon |  | $25.49 |  | Optional |  | 
 | Powerwerx SB50-PP45 SB50 Gray to PP45 Adapter Cable | 1 | Amazon | SB50-PP45 | $19.49 |  | Optional |  | 
 | YCIND 3/8" Ring Eyelet Terminal Battery Boost Cable Heavy-Duty 30A Fuse 12V/24V 12AWG Cord 3Ft | 1 | Amazon |  | $11.99 |  | Optional |  | 
 | Anderson Power Products SB50 Connector Kit, 50 Amps, 36V Gray Housing, w/ 6 AWG, 6319 (Pair) | 1 | Amazon | SB-50 | $9.99 |  | Optional |  | 

## Slide 17: Parts List Page 3 of 5
 | GAMA Electronics 30 Amp Toggle Switch DPDT 3 Position On-Off-On | 1 | Amazon |  | $17.95 |  | Optional
 | Xaugiry 1ft 10AWG Solar Weatherproof SAE Power Socket Sidewall Port + 1.3ft SAE Connector Extension Cable | 1 | Amazon |  | $14.99 |  | Optional
 | DAMAVO YM1218 Female USB C & USB A Dual Port Car Charger Socket Power Outlet Type C USB Car Charger Socket Waterproof with Cap | 1 | Amazon |  | $13.99 |  | Optional
 | 10pcs FR PVC Cover Flame Retardant Sleeve for ANDERSON Powerpole Connector Housing | 1 | Amazon |  | $8.99 |  | Optional
 | GS Power 100% Copper 10 AWG OFC Wire. 25 FT Red & 25 FT Black Bonded Cable | 1 | Amazon |  | $39.99 |  | Optional
 | 1 Pc, 8 X 8 Inch X 1/2 Inch Thick Plywood Squares-Thick | 1 | Amazon |  | $13.04 |  | Optional

## Slide 18: Parts List Page 4 of 5
 | USB C to 4.5mm Laptop Charging Cable Adapter Male Type C to DC 4.5 x 3.0mm Converter Braided 6.5ft Fast 100W | 1 | Amazon |  | $14.88 |  | Optional |  | 
 | QTEATAK 10Pack 5.5MM x 2.5MM DC Male Power Plug Solder Power Jack Adapter Connector and 10Pack DC Female 3Pin Panel | 1 | Amazon |  | $7.99 |  | Optional |  | 
 | Gowoops 5PCS 150W DC-DC 10-32V to 12-35V Step Up Boost Converter Module Adjustable Power Voltage | 1 | Amazon | Laptop PWR | $19.99 |  | Gowoops 5PCS 150W DC-DC 10-32V to 12-35V Step Up Boost Converter Module Adjustable Power Voltage | $19.99 | 
 | SolarEnz 30' Anderson Connector Extension Cable for Portable Solar Panel Kit 10AWG | 1 | Amazon |  | $56.60 |  | SolarEnz 30' Anderson Connector Extension Cable for Portable Solar Panel Kit 10AWG | $56.60 | 
 | Ratcheting Crimper for use with 15/30 and 45 Amp Powerpole Connectors | 1 | Amazon | TC-1 | $37.95 |  |  |  | 
 | 3drcparts SERMOS Anderson POWERPOLE Battery Charge 12AWG Cable Connector | 1 | Amazon |  | $8.40 |  |  |  | 

## Slide 19: Parts List Page 5 of 5
 | Powerwerx PanelPlateSB1 for Anderson SB50 Series Connectors | 1 | Powerwerx |  | $9.99 |  | SB1-Panel | $9.99 | Powerwerx
 | Powerwerx Powerpole Insertion, Removal & Extraction Tool | 1 | Powerwerx |  | $9.99 |  | Optional |  | 
 | Red/Black Bonded Zip Cord Easy ID Low Voltage Cable | 1 | Powerwerx | Wire-RB-12-25 | $24.09 |  | Optional |  | 
 | 150 Piece Assorted 15/30/45A Anderson Powerpole Case by Powerwerx | 1 | Powerwerx |  | $49.99 |  | Optional |  | 
 | Total Parts Cost not including shipping and Tax |  |  |  | $1,483.16 |  |  | $739.93 | 

## Slide 20: Configuration and Operational Hours
Link to Spreadsheet:
Ron's Park System.xlsx
Show calcs and discuss
Assumptions & Definitions
Tx/Rx Profile
Calcs
Solar Power Profile
Graph